## Slide 1: ENGI 301 Blue Light Disinfection System Proposal
09/25/22
Ariadna Gomez

## Slide 2: Background Information
What is being proposed: a blue light-based disinfection system
  This blue light sanitation system would ideally consist of a 3D printed box, inside of which the endoscope would be placed. Blue LED lights would be distributed all along the inner lining of the box so that the outer surface of the endoscope can be irradiated with blue light. The purpose of blue light (405 nm) is to eliminate the biofilm that forms along the length of the endoscope as a result of colonoscopy procedures, for instance. This project is based on information gathered through studies which have analyzed the effect of blue light on the reduction of certain types of biofilm and have confirmed it could be a meaningful innovation since blue light has achieved the reduction of biofilm in certain instances. The blue light disinfection system would not start until the lid of the box is closed to protect the user’s eyes, can be turned on or off using a button, and has a countdown timer.
    An alternative or additional idea to the one proposed above would be to: do a saline wash of the biopsy channel before blue light sterilization, and culture that wash solution. Then, irradiate the length of the biopsy channel with blue light for a period of time, do another saline wash of the scope and culture that wash. Use a camera to detect changes in the cultures over time and compare the growth between each condition.
    https://www.ncbi.nlm.nih.gov/pmc/articles/PMC6627448/ (Section 6 is the basis for these ideas)
  https://www.hackster.io/Arnov_Sharma_makes/uvc-box-a-diy-uv-sterilizer-f09b8f
  https://www.hackster.io/roboticsbangladesh/helmet-sterilization-box-74e029
Currently, there are no projects like this one on Hackster.io; there are UVC sterilizer projects which accomplish the same goal, but do not use the PocketBeagle/blue LEDs/or a camera to accomplish and determine whether sterilization was effective.

## Slide 3: System Block Diagram
OSD335x-SM SiP
P1_14 & P2_23 - 3.3V
LED 1 - 50
USB Port
USB Hub
USB Camera
I2C1_SCL
I2C1_SDA
SCL
SDA
VCC
GND
Hex Display
GPIO 59
Button
1k
3.3V
3.3V
3.3V
3.3V
2.2k

## Slide 4: Power Block Diagram
OSD335x-SM SiP
SYS 3.3V
LEDs 1 – 50 (each @ 20mA, up to 500 mA)
5V
5V
3.3 V
USB Port
USB Hub
USB Camera
I2C1_SCL
I2C1_SDA
SCL
SDA
VCC
GND
Hex Display
3.3V
3.3V
3.3V
2.2k
GPIO 59
Button
1k
3.3V

## Slide 5: Components / Budget
Component | Need to Buy | Cost
Blue LEDs: Adafruit Super Bright Blue 5mm LED (25 pack)) Or (DigiKey) QLSP04RBU - LED Lighting Color - Royal Blue 455nm (450nm ~ 460nm) 1212 (3030 Metric) | 25 pack Or 25 | $8 (Adafruit) $17.38 (DigiKey)
USB Camera with a light source: (SparkFun) 3-in-1 Waterproof USB Endoscope Inspection Camera | 1 | $21.95
PocketBeagle (already own) | 1 | - (Parts Kit)
Box to place endoscope during sterilization procedure | 1 | 3D print OEDK
Button | 1 | - (Parts Kit)
Hex Display (Timer) | 1 | - (Parts Kit)